## Slide 1
2017 Prius Prime Longitudinal Control with Man in the Middle ACC Override

## Slide 2
Man in the Middle Control Method
All CAN messages allowed to pass through except acceleration command
Block commanded acceleration from DSU and insert desired command to pass on to Vehicle CAN Gateway
Requires stock ACC to be turned on to gain longitudinal override control
  Override control can be disabled by switching ACC off using stock vehicle controls
Requires cutting of vehicle CAN wires to implement

## Slide 3
Man in the Middle
~
~
x
~
~
x
Prius CAN Diagram
CAN 0
Rx/Tx
CAN 1
Rx/Tx

## Slide 4
Bus Messages
*Acceleration Control - Exclude from gateway
*

## Slide 5
Acceleration Control
Arb ID 343 (Hex)
  ACCEL_CMD: Acceleration Command [m/s^2]
    Scale= 0.001, Offset = 0
    Signed 2’s complement integer
    Motorola Format
  SET_ME_1: must be set to 1 during override control
  The rest of the payload copied from Driving Support ECU (DSU) output message
  Checksum calculated based on payload in bytes 1-7

## Slide 6
Checksum
Byte 8 of message 343
Calculate using payload in bytes 1-7 and this equation:

## Slide 7
Checksum Example
Msg 343 = F2 54 63 40 00 00 00 __
Msg 343 => F2 54 63 40 00 00 00 37
Note: all numbers are hexadecimal numerals

## Slide 8
Acceleration Control Envelope
Some wheel slip occurring during ACC override
Acceleration based on wheel speed
Chart: 
Speed [mph]
Manual Driving